## Slide 1: NTGR Guest SSID Proposal
06.09.2014

## Slide 2: Agenda
Guest SSID Concept
Guest SSID Concept, cont.
Fast-Lan Guest SSID Concept
Resources Back-up Guest SSID Concept

## Slide 3: Guest SSID Concept
In addition to extender’s main SSID connecting to the Root AP, the “guest” SSID can connect to another Root AP. For the extender, it looks like multiple SSID support but the connected clients in the two sub-networks can’t reach each other.
Principle, “Main of STA connects to Main of Root AP” and “Guest of STA connects to Guest of Root AP”.
MTK
Dual-band concurrent Extender
5G Guest SSID
5G Main SSID
2.4G Guest SSID
2.4G Main SSID
STA
Root
AP
5G Guest SSID
2.4G Guest SSID
2.4G Main SSID
5G Main SSID

## Slide 4: Guest SSID Concept, cont.
If root AP doesn’t support Guest SSID, all Main and Guest SSID of STA connect to root AP through main SSID of root AP with each band.
MTK
Dual-band concurrent Extender
5G Guest SSID
5G Main SSID
2.4G Guest SSID
2.4G Main SSID
STA
Root
AP
2.4G Main SSID
5G Main SSID

## Slide 5: Fast-LAN Guest SSID Concept
Fast Lan, 2.4 or 5G service STA and another band connects to root AP. 2.4G and 5G all can reach max. performance.
MTK
Dual-band concurrent Extender
2.4G Guest SSID
2.4G Main SSID
STA
Root
AP
5G Guest SSID
5G Main SSID

## Slide 6: Resource Back-up Guest SSID Concept
Somehow 2.4G Guest of Root AP loses connection with root AP, 5G Guest of Root AP will back-up 2.4G Guest of STA.
Same idea of 5G Guest of Root AP loses connection with root AP, 2.4G Guest will back-up it.
MTK
Dual-band concurrent Extender
5G Guest SSID
5G Main SSID
2.4G Guest SSID
2.4G Main SSID
STA
Root
AP
5G Guest SSID
2.4G Guest SSID
2.4G Main SSID
5G Main SSID