## Slide 1: Rules of Wifi packet forwarding
2014.08.14 Annie/Rorscha/Arvin

## Slide 2: Resource Back-up Guest SSID Concept
Somehow 2.4G Guest of Root AP loses connection with root AP, 5G Guest of Root AP will back-up 2.4G Guest of STA.
Same idea of 5G Guest of Root AP loses connection with root AP, 2.4G Guest will back-up it.
MTK
Dual-band concurrent Extender
5G Guest SSID
5G Main SSID
2.4G Guest SSID
2.4G Main SSID
STA
Root
AP
5G Guest SSID
2.4G Guest SSID
2.4G Main SSID
5G Main SSID

## Slide 3: Establish Forwarding pair in ApCli Linkup/Linkdown
Normal Pair
  Supposed
    ra0/rai0/apcli0/apclii0 all are up
    apcli0 and apclii0 both are linked up to root APs
  “ra0” has the partner “apcli0”
  “rai0” has the partner “apclii0”
Link Recover
  If apcli0 becomes Linkdown, ra0 will change his partner to apclii0
    If apclii0 also becomes linkdown, ra0 has no partner.

## Slide 4: Establish SA table in Rx path
Module Rx
  Maintain the relationship table of SA (MAC address) and source entry (identity by net_device).
  source entry data structure: bitwise
    Each bit is a unique entry (ra0/rai0/apcli0/apclii0)

## Slide 5: Forwarding Rule - Rx
Prepare
  Rx Hooking function is needed
  Pre-defined net_device entry “代表號”
    e.g. always select 5g, apclii0 and rai0
Unicast Rx
  [1] If the net_device has just one partner,  forward this packet to partner net_device.
  [0] If no partner,  return this packet to driver with “module not handled” and driver will indicate it to br0. (let packet can be forwarded to eth0)
    If DA is unknown, flooding work is done by br0
  [>=2] If more than two partners,  return this packet to driver with “module not handled” and driver will indicate it to br0. Let br0 decide which entry to forward. (or by module, select the new one?)
Multicast/Broadcast Rx
  Check SA (MAC Address) in module Rx function
    If more than one bit is set on SA table
      If net_device is NOT the代表號 (not apclii0 && not rai0), DROP THIS PACKET.

## Slide 6: Forwarding Rule - Tx
Prepare
  Tx Hooking function is needed
Unicast Tx
  If SA hits on SA table but no wifi pair path exists  DROP THIS PACKET
Multicast/Broadcast Tx
  Always Tx
  If SA hits on SA table but no wifi pair path exists  DROP THIS PACKET

## Slide 7: Hooking Function in WiFi Driver
Driver Rx
  In announce_802_3_packet()
  Call wf_fwd_rx_hook with RTMP_IRQ_LOCK
Driver Tx
  In RTMPSendPackets()
  Call wf_fwd_tx_hook WITHOUT RTMP_IRQ_LOCK, otherwise SMP system will hang due to double-lock issue.

## Slide 8: Backup Slides

## Slide 9: TODO
DA is not necessary to check, right?
Do we have to handle the unknown address, for example, from net_device eth0 or lo?
  SA? Or DA?
  Note: we have no chance to check it in Rx path, unless hook into ethernet driver
Aging function of SA table
  we need to clear table when apcli0/apclii0 linkdown
  And additional aging timer?
What if ra0/rai0 down with rai0/raii0 up?

## Slide 10: Question 1
Rorscha, 8/13
  Unicast, net_device is apcli/apclii
  If more than one pair, which pair to forward?
MTK
Dual-band concurrent Extender
5G Main SSID
2.4G Main SSID
STA
Root
AP
5G Main SSID

## Slide 11: Answer 1
Handle in module Rx function
  發現多於1條路的時候 (根據 net_device, 搜尋對應的 pairs, 若確認pair數大於1時就進來判斷)
  According to DA, check SA table 看目前packet的DA出現在哪些 partner的後端
    If just one pair  just forwared
    If more than one pair  select the new one
      In Rx hooking function, also record current jeffies
    If no pair  return to driver, goto br0

## Slide 12: Question 2
Rorscha, 8/13
  Unicast rule: “If no partner, DROP THIS PACKET”
    No packet can be forwared to ethernet and lo

## Slide 13: Answer 2
Consider eth0 and lo, we should not drop the packet in Rx hook function.
但是要如何達到客戶要求? 現在是說，STA連上 rai0, 去ping 2.4G root Ap, 竟然ping通了
  Forward by br0
  Drop in Tx hook function, but how to?
    net_device is overwrited.
    SA table?
    Pair?